## Slide 1
Fast Multiplication Algorithm for Three Operands
(and more)
Esti Stein
Dept. of Software Engineering, Ort Braude College
Yosi Ben-Asher
Dept. of Computer Science, Haifa University

## Slide 2: The Goal
Accelerating the execution time of running programs, by reducing the time of basic operations, such as multiplication.

## Slide 3: Multiplication is heavily used in
Multimedia
Graphics
Radar equipment
Cryptology
and more..

## Slide 4: Why multiplication is a Complex problem
Given two integers a,b ( n digits each)
  a × b = a + a + .. + a ( b times)
a × b using Long multiplication:
  To multiply two numbers with n digits, the time complexity of multiplying two n-digit numbers using long multiplication is Θ(n2)

## Slide 5: Booth - The main algorithm used for multiplication:
Consider the following multiplication:
98765 * 9999
Four mults and adds are needed to compute the product.
The easy way:
98765 * 9999 =
98765 * (10000 – 1) = 98765 * 10000 – 98765

## Slide 6: Booth Algorithm - explanation
An efficient way to multiply two signed binary numbers expressed in 2's complement notation :
Reduces the number of operations by relying on blocks of consecutive 1's
Example:
Y  00111110 = Y  (25+24+23+22+21).
Y  00111110 =Y × (01000000-00000010) = Y  (26-21). One addition and one subtraction

## Slide 7: Booth algorithm - example

## Slide 8: E-Booth for three multiplicands
When multiplying two numbers, the multiplicand is shifted i times and added, if the ith bit of the multiplier is equal to '1'.
When multiplying three numbers, the multiplicand is shifted k times and added, if the jth bit of one multiplier is equal to '1' and the (k-j)th bit of the second multiplier is also equal to '1' .

## Slide 9: E-Booth (the idea - 1)
Let A = 0110 (6), X = 0011 (3), Y=0001 (1)
A = (1000–0010)
X = (0100-0001)
AX Y = (1000–0010)  (0100-0001) =
(00100000-00001000-00001000+00000010)Y
  Y is shifted to bit 1 and added (denoted by 1+)
  Y is shifted to bit 3 and subtracted (denoted by 3-)
  shifted to bit 3 and subtracted (3-)
  shifted to bit 5 and added (denoted by 5+).
This phase is building the vector

## Slide 10: E-Booth (the idea - 2)
Let A = 0110 (6), X = 0011 (3), Y=0001 (1)
(00100000-00001000-00001000+00000010)Y
Y is subtracted twice at location 3. This equals to subtracting Y once at location 4.
This brings us to consider simplifications (reductions), before applying add/subtrat Y.
In this example we will end up with:
(00100000-00010000+00000010)Y, and calculate

## Slide 11: E-booth – the algorithm (3)
Let Y, X and A be three n-bit integers
A – Primary multiplier
X – Secondary multiplier
Y – Multiplicand
Transform X and A to vectors VX, VA by applying:
VX=  ; VA= ; and let '◦' be the concatenation operation
In parallel for i = 1..n do begin {* apply the same to VA *}
(a) if Xi+1XiXi-1="010" then VX = "i+“◦VX
(b) if XiXi-1="10” then VX = "i-"◦VX
(c) if XiXi-1="01" then VX = "(i+1)+"◦VX
End;

## Slide 12: E-Booth - example (4)
Y=22=00010110 (multiplicand).
X=54=00110110 (multiplier).
A=29=00011101 (primary multiplier).
X = 0 0 1 1 0 1 1 0 A = 0 0 0 1 1 1 0 1
VX = (7+ 5- 4+ 2-) and VA = (6+ 3- 1+)
1+
3-
6+
2-
4+
5-
7+

## Slide 13: E-Booth - example(5)
Perform "Cartesian addition" Between VX and VA
OV=VXVA
OV = (13+ 11- 10+ 10- 2(8+) 8- 7- 6- 2(5+) 3- )
 ( 7+ 5- 4+ 2- ) =
8+ 6- 5+ 3-
10- 8+ 7- 5+
13+ 11- 10+ 8-
1+
3-
6+

## Slide 14: E-booth – example(6) simplification
The vector can be represnted as a histogram, where the aim is to create long sequences, allowing us to apply the Booth algorithm.
Original OV =
(13+ 11- 10+ 10- 2(8+) 8- 7- 6- 2(5+) 3-)
= (13+ 11- 8+ 7- 6- 2(5+) 3-)
= (13+ 11- 8+ 7- 3-)
= (13+ 11- 2(7+) 7- 3-)
Simplified OV = (13+ 11- 7+ 3-)

## Slide 15: E-booth – the algorithm (7) simplification
Implement a historam using the operation vector as an input. For every k(i)+ in the vector: (i)s is the x-coordinate , and k will be the y-coordinate.
For each pair k(i)+ and k( i)- (signs are opposite), delete both
Flatten the histogram by reducing the height of every bar to 1. Use the fact that k is always a sum of powers of 2.

## Slide 16: E-booth – the algorithm (8) simplification
As a result we are getting sequences of consequtive bars.
For sequences with (i)s and consecutive (i-1)ŝ .. (i-j) ŝ replace it with (i-j) s
Apply Booth on consecutive sequences replacing (i)s .. (i-j) s with (i+1)s and (i-j) ŝ

## Slide 17: E-booth – 4 multiplicands simplification – example (9)
(B)01011011×(A)00011101×(X)00110110×(Y)00000001 =(B)91×(A)29×(A)54×(Y)1

## Slide 18: E-booth – the algorithm (10) calculate
Let Sum=0,
for every (Vi)s
shift Y Vi times.
if s="+" then Sum = Sum + Vi
else Sum = Sum – Vi
0 0 0 1 0 1 1 0 Y (*multiplicand 22 *)
0 0 1 1 0 1 1 0 X (*multiplier 54 *)
0 0 0 1 1 1 0 1 A (*pr. Multiplier 29 *)
+ 0 0 0 1 0 1 1 0 (+13) Y shifted to bit 13
+ 1 1 1 1 1 1 1 1 1 1 0 1 0 1 0 (-11) Y 2’s complement shifted 11
+ 0 0 0 1 0 1 1 0 (+7) Y shifted to bit 7
+ 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 0 1 0 1 0 (-3) Y 2’s complement shifted 1
0 0 0 0 0 0 0 0 1 0 0 0 0 1 1 0 1 0 0 1 0 1 0 0 (* 22 54  29 = 34452 *)

## Slide 19: The Reconfigurable Mesh
2-dimensional processor array with reconfigurable bus system.
A set of 4-IO ports labeled N,E,S,W connect each PE to its 4 neighbors.
Each PE has locally controllable switches


## Slide 20: Reconfigurable Mesh (The Vector)

## Slide 21: Reconfigurable Mesh (The Matrix)

## Slide 22: Reconfigurable Mesh (The Matrix)

## Slide 23: Reconfigurable Mesh (After Simplifications)

## Slide 24: Relative improvement percentage per calculation group in a 16 bit scan

## Slide 25: Thank you!!!