## Slide 1: VHDL 4
Building blocks of a computer

## Slide 2: VHDL 4 Building blocks of a computer
Combinational circuit and sequential circuit
Building blocks of a computer.
Control units are state machines, which have Flip-flops, decoders, multiplexers etc.
Beware that , there are usually more than one way to design the same digital system in VHDL

## Slide 3: Combinational Vs. Sequential ciruits
Combinational circuit, it has no memory
  Example: decoder, encoder, inverter
Sequential circuit, it has memory
  Circuits that change state and output according to some conditions, (input or clock)
Examples:
Sequential
  Latch, Flip-flops (FFs) with asynchronous or synchronous reset;
Combinational
  tri state buffer; decoder; multiplexer, bi-directional buffer,

## Slide 4: A typical CPU
FFs=Flip-flops
A state machine
contains FFs
ALU
(state machine)
Control Unit
State machine
I/O control logic
(state machine)
Registers
(FFs)
data-bus
Transceivers
(bi-directional buffers )
Memory
Address bus
(latches)

## Slide 5: Use VHDL to make digital system building blocks
1) latch,
2) flipflop with asynchronous reset,
3) flipflop with synchronous reset,
4) tri state buffer,
5) decoder,
6) multiplexer,
7) bi-directional buffer,

## Slide 6: VHDL Exercise 4 1) Latch: when gate=1, output follows input (level sensitive)
library IEEE;--(ok vivado 2014.4)
use IEEE.STD_LOGIC_1164.ALL;
entity latch_ex is
port (gate, in1 : in std_logic;
out1 : out std_logic);
end latch_ex;
architecture latch_ex_arch of latch_ex is
begin
process (gate,in1)
begin
if (gate = '1') then
out1 <= in1;
end if;
end process;
end latch_ex_arch;
in1
gate
out1
Latch
1-bit memory
D Q
C
The process executes once
when ‘gate’ or ‘in1’ changes
sensitivity list
http://faculty.kfupm.edu.sa/COE/ashraf/RichFilesTeaching/COE022_200/Chapter4_1.htm, or P.72 Advanced Digital Design with the Veriolog HDL by M.D. Ciletti

## Slide 7: Exercise 4.1 on latch: draw q
in1
gate
q
q
In1
gate
Latch

## Slide 8: 2) Edge-triggered Flip-flop with asyn. reset : reset before clock statement
library IEEE;--(ok vivado 2014.4)
use IEEE.STD_LOGIC_1164.ALL;
entity dff_asyn is
port (in1,clock, asyn_reset: in std_logic;
out1 : out std_logic);
end dff_asyn;
architecture dff_asyn_arch of dff_asyn is
begin
process(clock, asyn_reset)
begin
if (asyn_reset = '1') then
out1 <= '0';
elsif clock = '1' and clock'event then
out1 <= in1;
end if;
end process;
end dff_asyn_arch;
sensitivity list
edge triggered clock or
rising_edge(clock)
clock
in1
Draw (out1)
Q
in1
clock
Edge (50%)
Clock triggered
FF
Explain the meaning
of “50 % clock trigger” for a Flip Flop.
asyn_reset
Asyn_reset is 0

## Slide 9: Exercise 4.3 on architecture dff_asyn_a When will line 9 be executed? Which is more powerful: clock or reset?
library IEEE;--(ok vivado 2014.4)
use IEEE.STD_LOGIC_1164.ALL;
entity dff_asyn is
port (in1,clock, asyn_reset: in std_logic;
out1 : out std_logic);
end dff_asyn;
architecture dff_asyn_arch of dff_asyn is
begin
process(clock, asyn_reset)
begin
if (asyn_reset = '1') then
out1 <= '0';
elsif clock = '1' and clock'event then
out1 <= in1;
end if;
end process;
end dff_asyn_arch;
For asynchronous reset flipflop
asyn_reset and clock
must be in the sensitivity list

## Slide 10: 3) Flip-flop with syn. reset: clock before reset statement
library IEEE;--(ok vivado 2014.4)
use IEEE.STD_LOGIC_1164.ALL;
entity dff_syn is
port (in1,clock, syn_reset: in std_logic;
out1 : out std_logic);
end dff_syn;
architecture dff_syn_arch of dff_syn is
--begin process(clock,syn_reset) -- 'syn_reset' can be removed,
begin process(clock) -- 'syn_reset' can be removed,
begin
if clock = '1' and clock'event then
if (syn_reset = '1') then
out1 <= '0';
else
out1 <= in1;
end if;
end if;
end process;
end dff_syn_arch;
syn_reset
clock
out1
D
in1
Discuss why syn_reset is not needed in the sensitivity list
edge triggered clock

## Slide 11: Difference between Syn. & Asyn. RESET flip-flops (FF)
The order of the statements inside the process determines Syn. or Asyn. reset
if clock = '1' and clock'event then
if (reset = '1') then
if (reset = '1') then
q <= '0';
elsif clock = '1' and clock'event then
Syn. Reset Flip-Flop (check clock first)
Asyn. Reset Flip-Flop (check reset first)

## Slide 12: Exercise 4.4 on different flip-flops
**In our course, by default all flip-flops are treated as 50% edge triggered flip-flops.
What is the difference between
  synchronous reset (syn-reset) flip-flops and
  asynchronous reset (asyn-reset) flip-flops?
Discuss the difference between a latch and a flip flop.

## Slide 13: 4) Tri state buffer: using when-else (Use capital letter big Z for float, Z is a reserved character)
library IEEE;--(ok vivado 2014.4)
use IEEE.STD_LOGIC_1164.ALL;
entity tri_ex is
port (in1, control : in std_logic;
out1 : out std_logic);
end tri_ex;
architecture tri_ex_arch of tri_ex is
begin
out1 <= in1 when control = '1' else 'Z';
end tri_ex_arch;
out1
control
in1
remember: Z is a scissor
Z=float

## Slide 14: A decoder (N bits --> 2N bits)
Picture from: http://www.safesdirect.com/safes/meilink/safes.html

## Slide 15: 5) Decoder: using if statements
library IEEE;--(ok vivado 2014.4)
use IEEE.STD_LOGIC_1164.ALL;
entity decoder_ex is
port (in1,in2 : in std_logic;
out00,out01,out10,out11 : out std_logic);
end decoder_ex;
architecture decoder_ex_arch of decoder_ex is
begin
process (in1, in2)
begin
if in1 = '0' and in2 = '0' then
out00 <= '1';
else
out00 <= '0';
end if;
if in1 = '0' and in2 = '1' then
out01 <= '1';
else
out01 <= '0';
end if;
in1
in2
out00
out10
out11
out01
sensitivity list
in='1' and in2='0', open the safe
case 2
case 1

## Slide 16: (contin.)Decoder
if in1 = '1' and in2 = '0' then
out10 <= '1';
else
out10 <= '0';
end if;
if in1 = '1' and in2 = '1' then
out11 <= '1';
else
out11 <= '0';
end if;
end process;
end decoder_ex_arch;
case 3 (open the safe)
case 4

## Slide 17: 6) Multiplexer (2N bits --> N bits) (the reverse of decoder)
library IEEE;--(vivado 2014.4 tested ok)
use IEEE.STD_LOGIC_1164.ALL;
entity mux is
port (in1,in2, ctrl : in std_logic;
out1 : out std_logic);
end mux;
architecture mux_arch of mux is
begin
process (in1, in2, ctrl)
begin
if ctrl = '0' then
out1 <= in1;
else
out1 <= in2;
end if;
end process; end mux_arch;
Mux
out1
in1
in2
crtl
in1
in2
out1
crtl

## Slide 18: Note:7) Bi-directional bus: using data flow concurrent statements
library IEEE;--(ok vivado 2014.4)
use IEEE.STD_LOGIC_1164.ALL;
entity inout_ex is
port (io1, io2 : inout std_logic;
ctrl : in std_logic);
end inout_ex;
architecture inout_ex_arch of inout_ex is
begin
io1 <= io2 when ctrl = '1' else 'Z';
io2 <= io1 when ctrl = '0' else 'Z';
end inout_ex_arch;
io1
ctrl
io2
concurrent statements

## Slide 19: Exercise 4.5 for Bi-directional bus
Crt=1, “io1” follows “io2_in”
Crt=0, “io2” follows “io1_in”
Plot io1 io2
Io1_in
io1
Io2_in
Io2
ctrl
io1
ctrl
io2
Io1_in
Io2_in
R=10K
R=10K

## Slide 20: Exercise 4.6
List whether the following circuits are sequential or combinational and discuss the reasons
Circuit name | Sequential or combinational | Condition for state change if sequential | discussion
latch |  |  | 
Flip flop |  |  | 
tri state buffer |  |  | 
Decoder |  |  | 
Multiplexer, |  |  | 
Bi-directional buffer |  |  | 

## Slide 21: (ANSWER ) Exercise 4.6
List whether the following circuits are sequential or combinational and discuss the reasons
Circuit name | Sequential or combinational | Condition for state change if sequential | discussion
latch | Sequential | Input state | Has memory
Flip flop | Sequential | Clock edge | Has memory
tri state buffer | combinational | N.A. | No memory
Decoder | combinational | N.A. | No memory
Multiplexer, | combinational | N.A. | No memory
Bi-directional buffer | combinational | N.A. | No memory

## Slide 22: Quick revision
You should know how to design
  asynchronous , synchronous reset flip-flops
  tri state buffers,
  Combination logics
    decoders,
    multiplexers,
    bi-directional buffers,

## Slide 23: Appendix: do variables in processes have memory. (Good practice: Initialize variables before use; assign values to variables from input first)
library IEEE;
use IEEE.std_logic_1164.all;
entity test is port (a,reset_v1: in std_logic;
b ,c: out std_logic); end test;
architecture test_arch of test is
begin
label_proc1: process (a,reset_v1)
variable v1 : std_logic;
begin
if reset_v1 ='1' then
v1:= not a;
end if;
b<=a;
c<=v1;
end process label_proc1;
end test_arch;
**The answer is yes. That means after a process is called, the state of a variable will be stored for the next time the process is being run again.
V1 stays at two different levels depending on previous result

## Slide 24: Turn VHDL into schematic
Use Schematic viewer in ISE project navigator

## Slide 25: How to represent binary and hex numbers
Type Standard logic( with initialized values):
  signal code_bit : std_logic := ‘1’; --for one bit , init to be ‘1’, or ‘0’
  signal codex : std_logic_vector (1 downto 0) :=“01”; -- 2-bit
  signal codey : std_logic_vector (7 downto 0) :=x“7e”; --8-bit hex 0x7e