3	Binary Adder

In this experiment, the student will become familiar with the operation of a 4-bit binary adder, and will also learn how to cascade two 4-bit binary adders to form an 8-bit binary adder.

I. 4-Bit Binary adder

The TA will program one of your 22V10 Programmable logic devices so  that it implements a 4-bit binary adder function.  The pinout for this device is:

- Pin 12 – GND,  Pin 24  -  Vcc.

- Four bit A input:    A(3): pin2, A(2): pin3, A(1): pin4, A(0): pin5

- Four bit B input      B(3): pin6, B(2): pin7, B(1): pin8, B(0): pin9

- Carry-In :  pin 10

- Four Bit Sum output:  Sum(3): pin22, Sum(2): pin21, Sum(1): pin20, Sum(0): pin19

- Carry Out:  pin 18

Unused inputs can be left unconnected.

The logic symbol for a 4 bit binary adder is shown below.  A(0) is the LSB (least significant bit) of A, A(3) is the MSB (Most Significant Bit) of A.

- Connect the 4 bit  Sum output of the adder to LEDs.  Connect COUT output to an LED.  Connect the two 4 bit inputs A[3:0], B[3:0] to switch inputs.  Use a wire connection to either GND or VCC for the CIN input as appropriate for testing.

- Fill in Table #1 in the lab data sheet for your circuit.

II. 8 Bit Binary adder

- Connect two of the 4-bit binary adder chips to form an 8-bit adder. Use the diagram below to guide you (the carry out of the first 4-bit adder becomes the carry-in of the 2nd four-bit adder).

Tie Cin to GND.  Tie 8 switch inputs to the A input (bits 7 down to 0).  Use connections to +5 v/ GND for the B inputs.

- Verify the operation of the 8 bit adder by applying the test inputs below (values are in DECIMAL).  Fill in Table #2 of the lab data sheet.

Two’s complement overflow could be a problem for some of the above additions. Which ones overflow the 8-bit range for two’s complement?

PRELAB Data page                TA Checkoff________

- Fill in the following table (Table #1)  for the operation of the 4-bit adder.

| Cin | A3 | A2 | A1 | A0 | B3 | B2 | B1 | B0 | S3 | S2 | S1 | S0 | Co |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 1 |  |  |  |  |  |
| 0 | 0 | 1 | 1 | 0 | 1 | 0 | 0 | 0 |  |  |  |  |  |
| 0 | 0 | 1 | 1 | 0 | 1 | 1 | 1 | 0 |  |  |  |  |  |
| 0 | 1 | 1 | 0 | 0 | 0 | 1 | 1 | 1 |  |  |  |  |  |
| 1 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 1 |  |  |  |  |  |
| 1 | 0 | 1 | 1 | 0 | 1 | 0 | 0 | 0 |  |  |  |  |  |
| 1 | 0 | 1 | 1 | 0 | 1 | 1 | 1 | 0 |  |  |  |  |  |
| 1 | 1 | 1 | 0 | 0 | 0 | 1 | 1 | 1 |  |  |  |  |  |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |  |  |  |  |  |
| 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 |  |  |  |  |  |

- Perform the binary addition operations in section III – 8 bit additions

Examples:

| Decimal | Binary |  | Decimal | Binary |
| --- | --- | --- | --- | --- |
| 36 | 00100100 |  | 53 | 00110101 |
| (+) 15 | 00001111 |  | (-) 19 | 11101101 |
| 51 | 00110011 |  | 34 | 00100010 |

Fill in the following values:

| Decimal | Binary |  | Decimal | Binary |
| --- | --- | --- | --- | --- |
| 56 |  |  | 75 |  |
| (+) 23 |  |  | +(-22) |  |

| Decimal | Binary |  | Decimal | Binary |
| --- | --- | --- | --- | --- |
| -53 |  |  | -65 |  |
| (+) (-42) |  |  | +(-80) |  |

## Lab Data Sheet                TA CHECKOFF______________

4-Bit Binary Adder (Table 1)

| Cin | A3 | A2 | A1 | A0 | B3 | B2 | B1 | B0 | S3 | S2 | S1 | S0 | Co |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 1 |  |  |  |  |  |
| 0 | 0 | 1 | 1 | 0 | 1 | 0 | 0 | 0 |  |  |  |  |  |
| 0 | 0 | 1 | 1 | 0 | 1 | 1 | 1 | 0 |  |  |  |  |  |
| 0 | 1 | 1 | 0 | 0 | 0 | 1 | 1 | 1 |  |  |  |  |  |
| 1 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 1 |  |  |  |  |  |
| 1 | 0 | 1 | 1 | 0 | 1 | 0 | 0 | 0 |  |  |  |  |  |
| 1 | 0 | 1 | 1 | 0 | 1 | 1 | 1 | 0 |  |  |  |  |  |
| 1 | 1 | 1 | 0 | 0 | 0 | 1 | 1 | 1 |  |  |  |  |  |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |  |  |  |  |  |
| 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 |  |  |  |  |  |

8-Bit Adder (Table 2):

|  | Binary |
| --- | --- |
| Decimal | CO | MSB 7 | 6 | 5 | 4 | 3 | 2 | 1 | LSB 0 |
| 56 | X |  |  |  |  |  |  |  |  |
| 23 | X |  |  |  |  |  |  |  |  |
| 75 | X |  |  |  |  |  |  |  |  |
| -22 | X |  |  |  |  |  |  |  |  |
| -53 | X |  |  |  |  |  |  |  |  |
| -42 | X |  |  |  |  |  |  |  |  |
| -65 | X |  |  |  |  |  |  |  |  |
| -80 | X |  |  |  |  |  |  |  |  |

# Text boxes

4 Bit Adder
Bus notation

Cout

4

4

4

Sum[3:0]

Cin

B[3:0]

A[3:0]

4 Bit Adder

Cout

Sum(0)

Sum(1)

Sum(2)

Sum(3)

B(0)

B(1)

B(2)

B(3)

A(0)

A(1)

A(2)

A(3)

Cin

Sum[7:0]

8

Sum[7:4]

Sum[3:0]

B[7:4]

B[3:0]

8

B[7:0]

A[7:4]

A[3:0]

A[7:0]

8

Cout

4

4

4

Sum[3:0]

Cin

B[3:0]

A[3:0]

8 Bit Adder from two 4-bit Adders 
 Bus notation is used in schematic

Cout

4

4

4

Sum[3:0]

Cin

B[3:0]

A[3:0]

b)    75
 +  (-22)
-----------

a)    56
 +    23
-----------

c)    -53
 +  (-42)
-----------

d)    -65
 +  (-80)
-----------