DIGITAL DESIGN COEN 312 Lecturer: Asim J. Al-Khalili

Answer All Questions. Time Allowed 1 hr. 10min. Midterm exam. Oct 14 , 2010

Sample A

Question 1 (Use Boolean Algebra for Question 1)

1.a  Simplify F:

F(A,B,C,D) = [AB + A’] . [AB + A’C + BC]’                                     (2 marks)

1.B  Simplify to obtain minimum SOP

F(W,X,Y,Z) = [XY ( (X +Y’)][(W      (W + Y)]                             (2 marks)

1.b  Simplify to obtain minimum SOP

F(a,b,c,d) = a’b’(c +d’)(1 + 0) + a’(c’d +cd’ +1) + (a’b + 0)cd        (2 marks)

1.c  Minimize the following circuit, draw final minimized circuit.

You have single rails available to you.                                              (2 marks)

Question 2

2.a  Give minimal SOP for F(a,b,c,d) given by the following K-map (2 marks)

Identify the Prime Implicants and Essential Prime Implicant clearly.

2.b   Give the POS of F(A,B,C,D) = (A + BD)(B +AD)   (1 mark)

2.c   Give the minterm list of F(A,B,C,D) = B                 (1 mark)

2.d   Give the minimal NOR-NOR implementation of

F(A,B,C,D) = AC’ + A(D + CB)                              (2 marks)

## Question 3

- Given function F1 given in the K-map below determine F2 using F1.

- Draw the final circuit of F2                            (  6 Marks  )

F1= A ( B  ( C ( D                                                          F2

Question 4

Draw the timing diagram for F(A,B,C)  for the following consecutive inputs:

ABC = 000, 010, 110, 010, 111  (**follow these vectors in order given).

Assume the following gate delays,

NAND =3ns,              OR gate = 4ns,                               (5 marks)

A

B                                                                       F

C

# Text boxes

00     01     11    10

00

01

11

10

1       1

1       X

X       1

1        1

ab

cd

1               1

1              1

1                 1

1                1

00     01     11    10

00

01

11

10

AB

CD

4 ns

a

a

3 ns

b

d

F

c

1       1                1

1               1

1        1       1      1

1        1

00     01     11    10

00

01

11

10

ab

cd